## Slide 1: Foundations for Good Floodplain Restoration in the Upper Mississippi River Basin to Improve Water Quality October 2018 UMRC
Brad Gordon
Lapham Fellow, River Restoration
Notes: Introduce self
Working with Olivia Dorothy and Eileen Shader in the UMRB on floodplain restoration

## Slide 2
Founded in 1973, American Rivers protects wild rivers, restores damaged rivers, and conserves clean water for people and nature.
Headquartered in DC, American Rivers has offices across the country and more than 200,000 supporters, members, and volunteers nationwide
Notes: Introduce American Rivers
national conservation organization
protect wild rivers, restore damaged rivers and conserve clean water for people and nature.
headquartered in DC but have staff throughout the country that work on our 11 priority river basins.
I work in our river restoration program with a focus on FPR. We work to facilitate floodplain restoration and reconnection projects through policy change, capacity building, and project implementation.

## Slide 3: Upper Mississippi River Basin Floodplain Restoration
Presentation Overview:
Multi-benefit Floodplain Restoration in the UMR
Nutrient Removal in floodplains
Policy and Practice
Notes: One of the river basins where we are focused on for floodplain work is the Upper Mississippi River and that’s what I’d like to talk about today.
quick overview of AR’s approach to floodplain restoration- importance of maximizing multiple benefits
I’m going to focus on our research into one benefit in particular- nutrient removal
  Science
  Project design
Touch on implementation of fpr projects that can reduce nutrients through project and practice.
Regional focus on UMR basin- MN, WI, IA, IL, MO

## Slide 4
Rivers Flood
Floods drive natural processes and ecosystem functions that sustain rivers and create floodplains.
Floodplains support natural functions
Notes: I like to start my presentations with a reminder that floods are natural!
Most people think of floods as a threat and are concerned about hazards and damages
As a river conservation organizations- we love floods because they are critically important to the health of a river.
Floodplains are valuable because they support natural functions as a result of periodic flooding.
Under natural flow conditions, most rivers have seasonal floods as result of rainier seasons or spring snowmelt.
Smaller frequent floods that occur on average every 2 to 5 years are very beneficial
Larger floods are important for the landscape changes
http://plattebasintimelapse.com/wp-content/uploads/2015/08/near-plum-creek-scoured-sandbars.jpg

## Slide 5
Benefits of a Connected Floodplain
Notes: What are some of the benefits of having a connected floodplain?

## Slide 6
…but this is what most floodplains look like.
Notes: But we have this instead in many places.

## Slide 7: Extent of floodplain disconnection
“
What we know:
Nationally, the USACE has 15,000 miles of levees in their National Levee Safety Database. That represents 10 percent of levees in the U.S.
  ~8000 miles in the Upper Mississippi basin
“To this day the amount, location and condition of agricultural levees across the UMRB are poorly documented, although there are nearly 5,000 known drainage districts in Illinois, Iowa, and Wisconsin.”
Notes: When we developed our Upper Mississippi plan, we performed a conservation assessment that identified floodplain disconnection as one of the most underserved issues in the basin.
While we don’t have exact numbers for the extent of floodplain disconnection in the basin, here are a few things we do know:
Nationally, no one, including the Army Corps, knows where all the levees are.
The 15,000 or so they have in their National Levee database represent only 10 percent of levees across the US.
This is because most levees were built by farmers back when the land was being settled. They straightened stream channels and dumped excess dirt up on the stream banks.
We do know there are about 5000 known drainage districts in IL, IA, and WI alone.
And it’s estimated that 25% of IL surface waters were modified directly by channelization or levee construction.
Sources:
1) Levees Everywhere image: The Times-Picayune, sourced from Levees.org, FEMA. 2010 http://levees.org/2010/01/03/the-new-orleans-region-and-its-levees-is-not-alone/
http://blog.nola.com/levees/2010/01/what_is_leveesorg.html
2) USACE Levee miles: USACE Levee Safety Program https://www.usace.army.mil/Missions/Civil-Works/Levee-Safety-Program/USACE-Program-Levees/
3) Implementing Nonstructural Solutions for Flood Management in the Upper Mississippi River Basin, Montgomery and Associates, prepared for American Rivers
4) Channelization and levee construction in Illinois: Review and implications for management. Mattingly, Rosanna, Edwin Herricks, and Douglas Johnston. Environmental Management. Nov 1993, Vol 17, Issue 6, p 781-795. https://link.springer.com/article/10.1007/BF02393899

## Slide 8
Notes: If we want this, what is the breakdown of the functions we’re trying to restore?

## Slide 9: Restoring Functional Floodplains
Floodplain Restoration Projects
Connectivity
Variable Flow
Spatial Scale
Habitat and Structural Diversity
How are floodplains restored?
Notes: One question we encounter all the time is “what is floodplain restoration?”
Not as simple as dam removal- the dam is there or it’s not. Floodplain restoration is more of a sliding scale based on the functions and benefits you want to achieve.
American Rivers is typically looking to maximize natural functions and we’ve concluded that means addressing these four attributes:
Connectivity- the water needs to be able to get onto the floodplain
Variable Flow- flows should be variable in timing, depth, and duration- important for species
Spacial Scale- big enough to have benefits
Habitat and Structural Diversity- appropriate diversity on the landscape, again species

## Slide 10: Floodplain reconnection and restoration techniques
Alter levees- setback, breach, remove
Install floodplain terrace
Flood bypass
Address causes of flow alteration
Restore floodplain activating flows
Address water withdrawals
Conservation easements
https://www.americanrivers.org/conservation-resource/reconnecting-floodplains/
Land acquisition
Land transfer
Passive restoration
Enhance woody debris
Riparian planting
Manage non-native species
Restore habitat diversity
Notes: What does this look like on the ground?
- Every project is unique and the specific actions that go into it are varied according to the needs and the specific benefits that you’re trying to achieve.
If we’re dealing with leveed floodplains, a key component would be to alter by removing it, breaching, setback, or if necessary a water control structure in order to allow water to get back onto the floodplain.
The photos show two examples of levee alterations- first is a levee in iowa that breached during a flood. The land behind was acquired and the levee left unrepaired to naturally erode over time.
The second is a levee setback, where the old levee close to the river was removed and reconstructed further from the river.
- If a floodplain is already connected, but it’s been in agriculture for decades, it might require some earth moving and planting to restore diverse land features- side channels, wetlands, and so on.

## Slide 11
Literature Review
Nutrient Reduction on Floodplains
Notes: We decided to look at the literature to see if it stood up to the assumptions.
Brad’s project- lit review of 200 studies- kind of small comparably but gives us a starting point for providing better estimates of nutrient reductions

## Slide 12
Compare Reductions
Chart: Conservation Practices in the Iowa Nutrient Reduction Strategy
| Fertilize with Manure | Fertilizer Timing | Nitrification Inhibitor | Fertilizer Rate | Cover Crops | Drain Water Mgt | Extended Rotations | Bioreactors | Saturated Buffer | Wetlands | Floodplains | Land Retirement
 | 0.5 | 5.5 | 9 | 10 | 30 | 33 | 42 | 43 | 50 | 52 | 60.4 | 85
Notes: If we compare floodplains to common best practices for removing N used by Upper Miss states, it turns our that floodplains are very effective.

## Slide 13
Compare Reductions
Chart: Conservation Practices in the Iowa Nutrient Reduction Strategy
| Fertilizer Rate | Floodplains | Fertilizer Placement | Conservation Tillage | Fertilize with Manure | Buffers | Land Retirement | Terraces | Sediment Control Basins | No Till (from chisel plow)
 | 8.8 | 26.4 | 30 | 33 | 46 | 58 | 75 | 77 | 85 | 90
Notes: Phosphorus results come in a bit lower when compared to other strategies but these results are a bit deceiving.
For one, these strategies are still the best of the best, so to fall in the top ten is a good result.
Second, the literature generally looks at floodplains designed with nitrate as the target nutrient, not phosphorus, so really any phosphorus reduction is a bonus.

## Slide 14: What should we restore for better nutrient removal?

## Slide 15
What should we restore for better nutrient removal?

## Slide 16
Target river & stream reaches with higher concentrations of nitrogen and phosphorus.

## Slide 17
Restore heterogeneity and geomorphic diversity. Avoid homogenous pools.

## Slide 18
Having vegetation and topography to improve sedimentation and accretion could be best for both nutrients’ particle-bound forms.
Notes: Harvesting vegetation is an option in some cases depending on the goals of the restoration.

## Slide 19
Where should we focus our efforts?
?

## Slide 20: Nitrate Removal in Floodplains: MRB Study Locations

## Slide 21: Is the Lower Mississippi Better?
Notes: Upper Mississippi River Basin may be more effective.
  Maybe higher concentrations?
  Closer to the source?
Local features will influence hydrology etc.

## Slide 22
Opportunities in Policy and Practice
Notes: The foundations for good floodplain restoration are limited by scientific knowledge, funding, and policies. What are we trying to do to get around these barriers?

## Slide 23: Research
Denitrification removed NO3--N ranging from 250 kg d-1 (March 2015) to 668 kg d-1 (October 2014).
Notes: So, we definitely need additional research into this topic to
- Better understand rates of nutrient cycling and sedimentation
- Better understand connections between size, location and concentration within the water column to design more effective projects
USGS and others in the UMR are engaged in monitoring nutrient management at floodplain restoration sites on the mainstem and tributaries such as Maquoketa River floodplain restoration site in IA
Hopefully we’ll see expansion in the literature in the next few years to inform policy and practice on the ground

## Slide 24: Policy Improvements
State nutrient reduction strategies
NRCS Easements
  ACEP- Wetland Reserve Easements
  CREP Wetlands
  EWP Floodplain Easements
Alternative crops in floodplains
Photo by Chris Young
Notes: State nutrient reduction strategies= floodplains are not their own practice. If they’re mentioned at all they are lumped together with all wetlands. Future updates should include floodplain restoration and reconnection as distinct practices
Funding via Farm Bill conservation projects
Currently, best option is EWP program floodplain easements- but these require congressional appropriation after a disaster.
Looking at options through other programs and addressing policies that deter floodplain restoration.
  For instance, Agricultural Conservation Easement Program funds easements. But states gear their ranking towards farmable and edge of field wetlands or ideal duck habitat. Lands that flood regularly or are vulnerable due to levee breach actually receive a lower ranking.

## Slide 25: Integration with Flood Management
2017 Fallow land
Notes: Here’s an example of how a lack of integration plays out on the ground.
Dogtooth bend is a site in southern IL where levees have breached about 8 times in the last 10 years. Major floods in 2016= levee breach was about a mile wide. Dumped sand across the bend. Massive dump of sediment and scouring that destroyed farmland.
Impact on farmers. 5500 acres of land that have applications in for wetland reserve and EWP easements, waiting for funding to come through. Brown areas are fallow land in 2017, farmers can’t get any yield.
Levee district did pool funds to build a cheaper version of the levee but still millions of $ to build. From what we know, farmers are still wanting easements. Too much sand and risk. We needed to have a funding source for buyouts available for this.

## Slide 26: Reconnecting Easements
Notes: This is an example of a floodplain in the Midwest that has an NRCS floodplain easement on a portion of the floodplain but still row crops next to it. The hydrology cannot be fully restored because this would flood the crops. This is a problem wherever there are floodplain or wetland easements. Only the vegetation can be restored with maybe a small wetland constructed inside the easement. Until all the land can tolerate flooding, this easement will be only partially restored.

## Slide 27: Reconnecting Easements
More research for alternative practices in the floodplain
  Perennial crops for wet areas?
  Better grazing options?
brewpublic.com
Notes: We need some of our alternative crop studies to focus on wet areas. Most are focus on upland and dry species. How do we graze well in a floodplain? What or forage species work well? What are some alternative markets that may allow for perennial species in an area we allow to flood?

## Slide 28: New Tools: AR’s Reconnecting Rivers to Floodplains Report
https://www.americanrivers.org/conservation-resource/reconnecting-floodplains/

## Slide 29
Brad Gordon, bgordon@amrivers.org
www.americanrivers.org
Notes: Our team is really excited about branching out into floodplain restoration. We think it’s critically important to reverse the trend of floodplain loss and we believe AR is the voice that can move floodplain restoration from an innovative approach to mainstream.