## Slide 1
The Floodplain Connection:
The Role of Small to Large Restored Wetlands in Improving Water Quality
Jill Kostel, PhD
Senior Environmental Engineer
The Wetland Initiative
jkostel@wetlands-initiative.org

## Slide 2
The Wetlands Initiative is a nonprofit dedicated to restoring the wetland resources of the Midwest to improve water quality, increase wildlife habitat and biodiversity, and reduce flood damage.

## Slide 3: Wetland values and functions
SERVICE | WETLANDS
Environmental Goods | Food Fresh Water Fuel
Regulating Services | Carbon Storage Climate Regulation Flood Regulation Groundwater Replenishment Water Quality Improvement Shoreline Stabilization Biodiversity/Wildlife Habitat
Support Services | Primary Production Nutrient Cycling Soil Formation
Cultural Services | Aesthetic Spiritual Educational Recreation

## Slide 4
BIG SPONGE (FLOOD STORAGE)

## Slide 5
WETLAND NUTRIENT DYNAMICS
(Symbols courtesy of the Integration and Application Network, University of Maryland Center for Environmental Science at ian.umces.edu/symbols/)

## Slide 6: Floodplain wetlands
Position and scale of floodplain wetlands (restored or constructed) for water quality improvement
Along main river channels on adjacent floodplain or behind levees
Within the headwaters areas of small watersheds
  On field edges between farm and receiving waters
  Within ditch or stream channel
TRIB TO ILLINOIS RIVER
Hydrologic connection to the floodplain and wetland areas
Natural hydrologic interaction
“Restored” connection
Designed hydrologic connection

## Slide 7: Scale of Floodplain wetlands
Floodplain of main-stem rivers
(large-scale restored wetlands)
Floodplain of headwater streams
(multiple, small-scale restored or created wetlands)
(NRCS)

## Slide 8: TWI Restoration project sites
Dixon Waterfowl Refuge (Hennepin, IL)
Little Calumet River Basin (near Gary, IN)
Springbrook #1, Phase 1 (Wheaton, IL)
SmartWetland sites (Big Bureau Creek Watershed, IL)
1
2
3
4

## Slide 9
OUTLET TO IL RIVER
1. SUE & WES DIXON WATERFOWL REFUGE
FORMER HENNEPIN LEVEE DRAINAGE DISTRICT (~50 YR LEVEL)

## Slide 10
1996 (PRE-RESTORATION)

## Slide 11
RESTORATION STARTED IN 2004
BIODIVERSITY DESIGN TARGET

## Slide 12: Water quality (No3-N)
Chart: Nitrate-Nitrogen (mg/L)
OPEN LAKE SAMPLES
SEEP (FIELD EDGE SAMPLES)
DISCHARGING LOWER NITRATE CONCENTRATIONS

## Slide 13: RECONNECTION TO ILLINOIS RIVER?
River stage level at Henry, IL
IT’S A DIFFERENT RIVER NOW
River Stage (feet NGVD 1929)
J
F
M
A
M
J
J
A
S
O
N
D
1870
440
430
435
445
450
455
438
1870 H&H
LAKE LEVEL
2014 H&H
LAKE LEVEL
438
1940 PEORIA DAM POOL
J
F
M
A
M
J
J
A
S
O
N
D
440
430
435
445
450
455
1993

## Slide 14: 2. Little calumet river basin

## Slide 15: Little calumet river basin
Protection of 3,500 acres of existing residential, industrial, and transportation uses
Flood protection up to 200 year level via set-back levees, levees, and floodwalls
2,000 acre river/recreation corridor

## Slide 16: Little calumet river basin
Opportunity to restore/enhance wetland areas for bird habitat

## Slide 17: Little calumet river basin
Chart: Little Calumet River Gauge Data, Lake Station IN Datum = 579.64 feet NAVD88 (1.1 miles downstream of MLK North Dam)
Note: yellow line = ~base flow blue line = top of MLKN dam | 0
MLKN DAM
BASE FLOW
MLKS POOL

## Slide 18
El. 587
El. 588
El. 589
El. 590

## Slide 19: 3. Springbrook #1
St. James Farm, Forest Preserve District of DuPage County

## Slide 20: Springbrook #1
TYPICAL URBAN STREAM SYSTEM: CHANNELIZED, INCISED, AND DRAINED

## Slide 21: Springbrook #1
WATERS OF U.S. MIGITATION SITE
2,800 linear ft reconnected with floodplain
2,000 linear ft remeandered
~3 acres wetland marsh restoration
Promote ground/surface water exchange
Improve connectivity

## Slide 22: Springbrook #1
STREAM AND FLOODPLAIN FUNCTION UPLIFT
BEFORE
BEFORE
AFTER
AFTER
Additional nutrient removal:
188 tons/yr sediment
188 lbs/yr phosphorous
377 lbs/yr nitrogen
Improved hydraulic connection between stream channel and floodplain at lower flow condition
(J. Marquez Reina, 2017)

## Slide 23
4. BIG BUREAU CREEK WATERSHED
CONSTRUCTED WETLANDS AS A NUTRIENT REDUCTION SOLUTION FOR TILED CROPLAND
(Bennett, BC SWCD)

## Slide 24: TILE DRAINAGE WETLANDS
Sited and designed to intercept agricultural runoff prior to ditch or stream
Created or constructed emergent marsh system
Located in riparian areas in the headwaters of smaller watersheds

## Slide 25
(Bennett, BC SWCD)
TILE INLET
Bureau County CW1 Highlights
2016:
2,425 lbs NO3-N, 220 lbs SRP
12% avg annual NO3-N removal
3.8% OM sediments (carbon)
2017:
1,323 lbs NO3-N 0 lbs SRP
35% avg annual NO3-N removal
5.2% OM sediments (carbon)

## Slide 26
(Kevin Bennett, BC SWCD)
TILE INLET
(Izadmehr, UIC)
Bureau County CW2 Highlights (2017-)
0.8 acre treatment wetland
~30 acres tile drainage captured
64% avg annual NO3-N removal
7.1% OM sediments (hydric soils)
(Bennett, BC SWCD)

## Slide 27: Farm runoff wetlands
Iowa Department of Agriculture and Land Stewardship
CREP Nutrient Removal Wetland
The Nature Conservancy Mackinaw River Watershed
(Des Moines Register, 2015)
(Kirkham, TNC)

## Slide 28
www.wetlands-initiative.org